## Slide 1: Announcement
Project #1 due today
Assignment #3 release today
  To be released at 11:59am
  Due Nov.9 11:59pm
Project #2 to be released next Tuesday
  To be released at Nov.2 11:59am
  Due Nov.16 11:59pm

## Slide 2: Intro to Networking and ARP

## Slide 3: Today: Intro to Networking
Internet: A global network of computers
OSI model: A layered model of protocols

## Slide 4: What’s the Internet?

## Slide 5: What’s the Internet?
Network: A set of connected machines that can communicate with each other
  Machines on the network agree on a protocol, a set of rules for communication
Internet: A global network of computers
  The web sends data between browsers and servers using the Internet
  The Internet can be used for more than the web (e.g. SSH)

## Slide 6: Protocols
A protocol is an agreement on how to communicate that specifies syntax and semantics
  Syntax: How a communication is specified and structured (format, order of messages)
  Semantics: What a communication means (actions taken when sending/receiving messages)
Example: Protocol for asking a question in lecture?
The student should raise their hand
The student should wait to be called on by the speaker or wait for the speaker to pause
The student should speak the question after being called on or after waiting

## Slide 7: Layering: The OSI Model

## Slide 8: Layering
Internet design is partitioned into various layers. Each layer…
  Has a protocol
  Relies on services provided by the layer below it
  Provides services to the layer above it
Analogous to the structure of an application and the “services” that each layer relies on and provides
Code You Write
Run-Time Library
System Calls
Device Drivers
Voltage Levels/Magnetic Domains
Fully isolated from user programs

## Slide 9: Example: Sending Mail
Alice
Bob
I am hungry.

## Slide 10: Example: Sending Mail
Alice
Bob
Send to: Bob
I am hungry.

## Slide 11: Example: Sending Mail
Alice
Bob
Mail to: 123 Bob St
Send to: Bob
I am hungry.

## Slide 12: Example: Sending Mail
Alice
Bob
Mail to: 123 Bob St
Send to: Bob
I am hungry.

## Slide 13: Example: Sending Mail
Alice
Bob
Send to: Bob
I am hungry.

## Slide 14: Example: Sending Mail
Alice
Bob
I am hungry.

## Slide 15: Example: Sending Mail
Alice
Bob
Each layer communicates with each other, relying on abstractions below them!
Relies upon: Sending messages to people
Provides: Sending messages to people
Relies upon: Sending messages to addresses
Provides: Sending messages to addresses

## Slide 16: OSI Model
Application
Transport
(Inter) Network
Link
Physical
1
2
3
4
7
OSI model: Open Systems Interconnection model, a layered model of Internet communication
  Originally divided into 7 layers
    But layers 5 and 6 aren’t used in the real world, so we ignore them
    And we’ll talk about layer 4.5 for encryption later
Same reliance upon abstraction
  A layer can be implemented in different ways without affecting other layers
  A layer’s protocol can be substituted with another protocol without affecting other layers

## Slide 17: Layer 1: Physical Layer
Provides: Sending bits from one device to another
  Encodes bits to send them over a physical link
    Patterns of voltage levels
    Photon intensities
    RF modulation
Examples
  Wi-Fi radios (IEEE 802.11)
  Ethernet voltages (IEEE 802.3)
Physical
1
Application
Transport
(Inter) Network
Link
2
3
4
7

## Slide 18: Layer 1: Physical Layer
Physical
1
Application
Transport
(Inter) Network
Link
2
3
4
7
A
B
01110111…01
Physical layer: “How do I transmit this sequence of 0’s and 1’s from A to B?”
Next: How do we talk to more than one device?

## Slide 19: Layer 2: Link Layer
Provides: Sending frames directly from one device to another
  Relies upon: Sending bits from one device to another
  Encodes messages into groups of bits called “frames”
Examples
  Ethernet frames (IEEE 802.3)
Physical
1
Application
Transport
(Inter) Network
3
4
7
Link
2

## Slide 20: Layer 2: Link Layer
Local area network (LAN): A set of computers on a shared network that can directly address one another
  Consists of multiple physical links
Frames must consist of at least 3 things:
  Source (“Who is this message coming from?”)
  Destination (“Who is this message going to?”)
  Data (“What does this message say?”)
Source: A
Destination: C
“Hello, this is A…”
A
B
D
C
Notes: The data link layer is concerned with local delivery of frames between nodes on the same level of the network.
Data-link frames, as these protocol data units are called, do not cross the boundaries of a local area network. Inter-network routing and global addressing are higher-layer functions, allowing data-link protocols to focus on local delivery, addressing, and media arbitration.

## Slide 21: Layer 2: Link Layer
In reality, computers aren’t all connected to the same wire
  Instead, local networks are a set of point-to-point links
However, Layer 2 still allows direct addressing between any two devices
  Enabled by transmitting a frame across multiple physical links until it reaches its destination
  Provides an abstraction of a “everything is connected to one wire”
Source: A
Dest: C
“Hello, this is A…”
A
B
C
D
E

## Slide 22: Ethernet and MAC Addresses
Source MAC Address (6 bytes) |  |  |  |  | 
Destination MAC Address (6 bytes) |  |  |  |  | 
VLAN Tag (4 bytes) |  |  |  | Type (2 bytes) | 
Data (variable-length) |  |  |  |  | 
Ethernet header
Notes: TODO: Nick made this a white slide, but should it be?

## Slide 23: Ethernet and MAC Addresses
Ethernet: A common layer 2 protocol that most endpoint devices use
MAC address: A 6-byte address that identifies a piece of network equipment (e.g. your phone’s Wi-Fi controller)
  Stands for Media Access Control, not message authentication code
  Typically represented as 6 hex bytes: 13:37:ca:fe:f0:0d
  The first 3 bytes are assigned to manufacturers (i.e. who made the equipment)
    This is useful in identifying a device
  The last 3 bytes are device-specific

## Slide 24: Layer 2: Link Layer
Physical
1
Application
Transport
(Inter) Network
3
4
7
Link
2
Source: A
Dest: C
“Hello, this is A…”
Link layer: “How do I transmit this frame from A to C, making sure that no one else thinks the message is for them?”
Next: How do we address every device in existence?
A
B
D
C

## Slide 25: Layer 3: Network Layer
Physical
Provides: Sending packets from any device to any other device
  Relies upon: Sending frames directly from one device to another
  Encodes messages into groups of bits called “packets”
  Bridges multiple LANs to provide global addressing
Examples
  Internet Protocol (IP)
1
Application
Transport
4
7
(Inter) Network
3
Link
2

## Slide 26: Layer 3: Network Layer
Recall the ideal layer 2 model: All devices can directly address all other devices
  This would not scale to the size of the Internet!
Instead, allow packets to be routed across different devices to reach the destination
  Each hop is allowed to use its own physical and link layers!
Basic model:
  Is the destination of the packet directly connected to my LAN?
    Pass it off to Layer 2
  Otherwise, route the packet closer to the destination
A
B
D
C
E
F
G
H
Router

## Slide 27: Layer 3: Network Layer
A
Router
C
D
E
B
Router
Router
Router
Router
Router
Router
Source: A
Destination: D
“Hello, this is A…”

## Slide 28: Layer 3: Network Layer
A
Router
C
D
E
B
Router
Router
Router
Router
Router
Router
Source: A
Destination: D
“Hello, this is A…”
This link could be Wi-Fi
And this link could be Ethernet
But the Internet protocol stays the same, end to end

## Slide 29: Layer 3: Network Layer
Packets must consist of at least 3 things:
  Source (“Who is this message coming from?”)
  Destination (“Who is this message going to?”)
  Data (“What does this message say?”)
  Similar to frames (layer 2)
Packets may be fragmented into smaller packets
  Different links might support different maximum packet sizes
  Up to the recipient to reassemble fragments into the original packet
  In IPv4, any node may fragment a packet if it is too large to route
  In IPv6, the sender must fragment the packet themselves
Each router forwards a given packet to the next hop
Packets are not guaranteed to take a given route
  Two packets with the same source and destination may take different routes
Notes: Ask: Why take different routes? What might happen?

## Slide 30: Internet Protocol (IP)
Version (4 bits) |  | Header Length (4 bits) |  | Type of Service (6 bits) |  |  | ECN (2 bits) | Total Length (16 bits) |  |  |  |  |  |  | 
Identification (16 bits) |  |  |  |  |  |  |  | Flags (3 bits) |  | Fragment Offset (13 bits) |  |  |  |  | 
Time to Live (8 bits) |  |  |  | Protocol (8 bits) |  |  |  | Header Checksum (16 bits) |  |  |  |  |  |  | 
Source Address (32 bits) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Destination Address (32 bits) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Options (variable length) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Data (variable length) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
IPv4 header
Notes: Notice: Source address, destination address, header checksum, fragment offset, and data

## Slide 31: Internet Protocol (IP)
Internet Protocol (IP): The universal layer-3 protocol that all devices use to transmit data over the Internet
IP address: An address that identifies a device on the Internet
  IPv4 is 32 bits, typically written as 4 decimal octets, e.g. 35.163.72.93
  IPv6 is 128 bits, typically written as 8 groups of 2 hex bytes: 2607:f140:8801::1:23
    If digits or groups are missing, fill with 0’s, so 2607:f140:8801:0000:0000:0000:0001:0023
  Globally unique from any single perspective
    For now, you can think of them as just being globally unique
  IP addresses help nodes make decisions on where to forward the packet

## Slide 32: Reliability
Reliability ensures that packets are received correctly or, if random errors occur, not at all
  This is implemented with a checksum
  However, there is no cryptographic MAC, so there are no guarantees if an attacker modifies packets
IP is unreliable and only provides a best effort delivery service, which means:
  Packets may be lost (“dropped”)
  Packets may be corrupted
  Packets may be delivered out of order
It is up to higher level protocols to ensure that the connection is reliable

## Slide 33: Layer 3: Network Layer
A
Router
C
D
E
B
Router
Router
Router
Router
Router
Router
Source: A
Destination: D
“Hello, this is A…”
Layer 3: “How do I get this packet from A to D?”
Next: How do we reliably send any length of data, not just packets?

## Slide 34: Layer 4: Transport Layer
Provides: Transportation of variable-length data from any point to any other point
  Relies upon: Sending packets from any device to any other device
  Builds abstractions that are useful to applications on top of layer 3 packets
Useful abstractions
  Reliability: Transmit data reliably, in order
  Ports: Provide multiple “addresses” per real IP address
Examples
  TCP: Provides reliability and ports
  UDP: Provides ports, but no reliability
  We’ll talk a lot about these protocols soon!
Physical
1
Application
7
Link
2
(Inter) Network
3
Transport
4

## Slide 35: Layer 4: Transport Layer
A
D
I am now sending an arbitrary length message that will probably be broken into several packets…
Unreliable Internet
Layer 4: “How do I transport this arbitrary data over an unreliable medium?”

## Slide 36: Layer 7: Application Layer
Provides: Applications and services to users!
  Relies upon: Transportation of variable-length data from any point to any other point
Every online application is Layer 7
  Web browsing
  Online video games
  Messaging services
  Video calls (Zoom)
Physical
1
Link
2
(Inter) Network
3
Transport
4
Application
7

## Slide 37: Layers of Abstraction and Headers
As you move to lower layers, you wrap additional headers around the message
As you move to higher layers, you peel off headers around the message
When sending a message we go from the highest to the lowest layer
When receiving a message we go from the lowest to highest layer

## Slide 38: Example: HTTP Request
HTTP
TCP
IP
Ethernet
Wires
HTTP
TCP
IP
Ethernet
Wires
GET / HTTP/1.1
...

## Slide 39: Example: HTTP Request
HTTP
TCP
IP
Ethernet
Wires
HTTP
TCP
IP
Ethernet
Wires
From: Port 1234
To: Port 80
GET / HTTP/1.1
...

## Slide 40: Example: HTTP Request
HTTP
TCP
IP
Ethernet
Wires
HTTP
TCP
IP
Ethernet
Wires
From: 1.2.3.4
To: 5.6.7.8
From: Port 1234
To: Port 80
GET / HTTP/1.1
...
Final destination

## Slide 41: Example: HTTP Request
HTTP
TCP
IP
Ethernet
Wires
HTTP
TCP
IP
Ethernet
Wires
From: 20:61:84:3a:a9:52
To: 6d:36:ff:4a:32:92
From: 1.2.3.4
To: 5.6.7.8
From: Port 1234
To: Port 80
GET / HTTP/1.1
...
Address of next hop

## Slide 42: Example: HTTP Request
HTTP
TCP
IP
Ethernet
Wires
HTTP
TCP
IP
Ethernet
Wires
From: 20:61:84:3a:a9:52
To: 6d:36:ff:4a:32:92
From: 1.2.3.4
To: 5.6.7.8
From: Port 1234
To: Port 80
GET / HTTP/1.1
...
Converted into bits and transmitted

## Slide 43: Example: HTTP Request
HTTP
TCP
IP
Ethernet
Wires
HTTP
TCP
IP
Ethernet
Wires
From: 89:8d:33:25:47:24
To: d5:a9:20:68:e0:80
From: 1.2.3.4
To: 5.6.7.8
From: Port 1234
To: Port 80
GET / HTTP/1.1
...
Received over the physical medium
Notice: The MAC addresses changed because the recipient is on a different network

## Slide 44: Example: HTTP Request
HTTP
TCP
IP
Ethernet
Wires
HTTP
TCP
IP
Ethernet
Wires
From: 89:8d:33:25:47:24
To: d5:a9:20:68:e0:80
From: 1.2.3.4
To: 5.6.7.8
From: Port 1234
To: Port 80
GET / HTTP/1.1
...

## Slide 45: Example: HTTP Request
HTTP
TCP
IP
Ethernet
Wires
HTTP
TCP
IP
Ethernet
Wires
From: 1.2.3.4
To: 5.6.7.8
From: Port 1234
To: Port 80
GET / HTTP/1.1
...

## Slide 46: Example: HTTP Request
HTTP
TCP
IP
Ethernet
Wires
HTTP
TCP
IP
Ethernet
Wires
From: Port 1234
To: Port 80
GET / HTTP/1.1
...

## Slide 47: Example: HTTP Request
HTTP
TCP
IP
Ethernet
Wires
HTTP
TCP
IP
Ethernet
Wires
GET / HTTP/1.1
...

## Slide 48: Example: HTTP Request
HTTP
TCP
IP
Ethernet
Wires
HTTP
TCP
IP
Ethernet
Wires
Relies upon: Transport of data
Provides: Transport of data
Relies upon: Global packet delivery
Provides: Global packet delivery
Relies upon: Local frame delivery
Provides: Local frame delivery
Relies upon: Communication of bits
Provides: Communication of bits

## Slide 49: Summary: Intro to Networking
Internet: A global network of computers
  Protocols: Agreed-upon systems of communication
OSI model: A layered model of protocols
  Layer 1: Communication of bits
  Layer 2: Local frame delivery
    Ethernet: The most common Layer 2 protocol
    MAC addresses: 6-byte addressing system used by Ethernet
  Layer 3: Global packet delivery
    IP: The universal Layer 3 protocol
    IP addresses: 4-byte (or 16-byte) addressing system used by IP
  Layer 4: Transport of data (more on this next time)
  Layer 7: Applications and services (the web)
Application
Transport
(Inter) Network
Link
Physical
1
2
3
4
7

## Slide 50: Next: Low-Level Network Attacks
Network Attackers
  Man-in-the-middle attacker
  On-path attacker
  Off-path attacker
ARP: Translate IP addresses to MAC addresses
DHCP: Get configurations when first connecting to a network
WPA: Communicate securely in a wireless local network

## Slide 51: Network Attackers

## Slide 52: Types of Network Attackers
 | Can modify or delete packets | Can read packets
Man-in-the-middle/In-path attacker | ✓ | ✓
Man-on-the-side/On-path attacker |  | ✓
Off-path attacker |  | 
Threat model: There are 3 types of attackers we’ll consider

## Slide 53: Spoofing
Spoofing: Lying about the identity of the sender
  Example: Mallory sends a message and says the message is from Alice
  The attacker can lie about the source address in the packet header
All types of attackers can spoof packets
  However, some spoofing attacks may be harder if the attacker can’t read or modify packets

## Slide 54: Real-World On-Path Attackers
How might a real-life attacker read packets?
Layer 1 attack: Use a special device to read bits being transmitted across space

## Slide 55: Real-World On-Path Attackers
Operation Ivy Bells | 
Matthew Carle | February 6, 2017
In an effort to alter the balance of the Cold War, divers from the USS Halibut scoured the ocean floor for a five-inch diameter cable that carried secret Soviet communications between military bases. The divers found the cable and installed a listening device. Upon their return to the United States, the NSA analyzed the recordings and found that a surprising amount of sensitive Soviet information travelled through the lines without encryption. The original tap was later discovered by the Soviets and is now on exhibit at the KGB museum in Moscow. | 
Notes: https://www.military.com/history/operation-ivy-bells.html

## Slide 56: Real-World On-Path Attackers
Layer 2 attack: Read packets sent across the local area network (LAN)
Recall: A LAN is a network of connected machines
  Any machine on the LAN can send packets to any other machine on the LAN
Some LANs use broadcast technologies
  Every packet gets sent to every machine on the LAN
  Each machine agrees to ignore packets where the destination is a different machine
A machine can break the agreement and read packets meant for other machines
  This is called promiscuous mode
  May require root access on the machine
A
B
D
C

## Slide 57: Real-World On-Path Attackers
tcpdump: A program for reading packets on the local network
  Uses promiscuous mode to read other machines’ packets in broadcast technologies
Wireshark: A graphical user interface (GUI) for analyzing tcpdump packets

## Slide 58: Real-World On-Path Attackers
Some layer 2 (Ethernet) devices can be configured to also send a copy of every packet to the attacker
  Many switches support this through “port mirroring”
  Or you can use dedicated Ethernet taps
Example: DualComm ETAP-2003
  Cost: $200
  Powered with USB (no extra power supply needed)
  ETAP-2003R extra fun: Attacker can also send packets
Ethernet Device
Attacker
Bob
Alice
To: Bob
“Hi”
To: Bob
“Hi”
To: Bob
“Hi”

## Slide 59: The Law and Sniffing Packets
You are allowed to sniff packets on your own network
  After all, it is your computers you are using
  Network administrators are allowed for network operation
  Strongly encourage you to do so at home and see what you see!
It is both grossly immoral and highly illegal to sniff traffic otherwise
  It is called “wiretapping”
So do not do this at Starbucks or other networks
  Unless you add a filter to only include packets to/from your computer for debugging purposes

## Slide 60: Address Resolution Protocol (ARP)

## Slide 61: Review: Layer 2 and Layer 3
Local area network (LAN): A set of machines connected in a local network
  The MAC identifies devices on layer 2
Internet protocol (IP): Many LANs connected together with routers
  The IP identifies devices on layer 3
A
B
D
C
E
F
G
H
Router

## Slide 62: Address Resolution Protocol (ARP)
ARP: Translates layer 3 IP addresses to layer 2 MAC addresses
  Example: Alice wants to send a message to Bob on the local network, but Alice only knows Bob’s IP address (1.2.3.4). To use layer 2 protocols, she must learn Bob’s MAC address.
Steps of the protocol
  Alice checks her cache to see if she already knows Bob’s MAC address.
  If Bob’s MAC address is not in the cache, Alice broadcasts to everyone on the LAN: “What is the MAC address of 1.2.3.4?”
  Bob responds by sending a message only to Alice: “My IP is 1.2.3.4 and my MAC address is ca:fe:f0:0d:be:ef.” Everyone else does nothing.
  Alice caches Bob’s MAC address.

## Slide 63: Address Resolution Protocol (ARP)
Alice
Bob
Charlie
Dave
Router
Alice’s cache | 
IP | MAC
1. Alice checks her cache to see if she already knows the MAC address corresponding to 1.2.3.4.
Alice knows Bob’s IP address (1.2.3.4) but wants to learn Bob’s MAC address.
Since her cache is empty, she must make a request to find out.

## Slide 64: Address Resolution Protocol (ARP)
Alice
Bob
Charlie
Dave
Router
Alice’s cache | 
IP | MAC
2. Alice asks everyone else on the local network: “What is the MAC address of 1.2.3.4?”
Alice knows Bob’s IP address (1.2.3.4) but wants to learn Bob’s MAC address.

## Slide 65: Address Resolution Protocol (ARP)
Alice
Bob
Charlie
Dave
Router
Alice’s cache | 
IP | MAC
3. Bob responds: “My IP is 1.2.3.4 and my MAC address is ca:fe:f0:0d:be:ef.”
Alice knows Bob’s IP address (1.2.3.4) but wants to learn Bob’s MAC address.
Everybody else ignores the request.

## Slide 66: Address Resolution Protocol (ARP)
Alice
Bob
Charlie
Dave
Router
Alice’s cache | 
IP | MAC
1.2.3.4 | ca:fe:f0:0d:be:ef
4. Alice adds Bob’s MAC address to her cache.
Alice knows Bob’s IP address (1.2.3.4) but wants to learn Bob’s MAC address.

## Slide 67: Address Resolution Protocol (ARP)
If Bob is outside of the LAN, Alice knows this
  Bob’s IP is not on the same “subnet” as Alice
But Alice knows the IP address of the “Gateway router”
  Recall: The router’s job is to make sure that the packet will be forwarded towards Bob (Layer 3)
So instead Alice generates an ARP request for the gateway router
  Layer 2 MAC address of the frame is set to the router
  Layer 3 IP address of the packet remains set as Bob's
  The router will forward the packet to some other LAN to get it closer to Bob
Notes: TODO Nick’s slide from FA21

## Slide 68: Attacks on ARP
Alice
Bob
Charlie
Mallory
Router
Alice’s cache | 
IP | MAC
1. Alice checks her cache to see if she already knows the MAC address corresponding to 1.2.3.4.
Alice knows Bob’s IP address (1.2.3.4) but wants to learn Bob’s MAC address.
Since her cache is empty, she must make a request to find out.

## Slide 69: Attacks on ARP
Alice
Bob
Charlie
Mallory
Router
Alice’s cache | 
IP | MAC
Alice knows Bob’s IP address (1.2.3.4) but wants to learn Bob’s MAC address.
2. Alice asks everyone else on the local network: “What is the MAC address of 1.2.3.4?”

## Slide 70: Attacks on ARP
Alice
Bob
Charlie
Mallory
Router
Alice’s cache | 
IP | MAC
3. Before Bob’s response can arrive, Mallory sends a malicious response: “My IP is 1.2.3.4 and my MAC address is 66:66:66:66:66:66.”
Alice knows Bob’s IP address (1.2.3.4) but wants to learn Bob’s MAC address.

## Slide 71: Attacks on ARP
Alice
Bob
Charlie
Mallory
Router
Alice’s cache | 
IP | MAC
1.2.3.4 | 66:66:66:66:66:66
4. Alice adds Mallory’s malicious address to her cache.
Alice knows Bob’s IP address (1.2.3.4) but wants to learn Bob’s MAC address.

## Slide 72: Attack: ARP Spoofing
Alice has no way of verifying the ARP response
  Spoofing: Any attacker on the network can claim to have the requested IP address
Alice is only expecting one machine to respond, so she will accept the first response
  Race condition: As long as the attacker responds faster, the requester will accept the attacker’s response
ARP spoofing requires Mallory to be in the same LAN as Alice
ARP spoofing lets Mallory become a man-in-the-middle (MITM) attacker
  Alice thinks that Bob’s MAC address is 66:66:66:66:66:66 (Mallory’s MAC address)
  When Alice sends a message to Bob, she is actually sending the message to Mallory
  Mallory can modify the message and then send the modified message to Bob

## Slide 73: ARP Spoofing: Defenses
Network switches
  When Alice wants to send a message to Bob, she sends the message to a switch on the LAN
  The switch maintains a cache of MAC to port (physical connection) mappings
  If Bob’s MAC address is in the cache, the switch sends the message directly to Bob
  Otherwise, the switch broadcasts the message to all computers
    Greatly improves efficiency as now the L1 network is no longer a shared media
Enterprise-class switches have additional optional features
  Security: An additional IP/MAC cache that responds first, preventing the attacker from seeing repeated requests
  Security: Only authorized MAC addresses can connect to specific ports—access control
  Isolation: Virtual local area networks (VLANs), which splits a single LAN into isolated parts
Tools like arpwatch track ARP responses and make sure that there is no suspicious activity
Notes: TODO Nick slide from FA21