## Slide 1: Transmission Control Protocol (TCP)

## Slide 2: Today: Transport Layer Protocols
Transmission Control Protocol (TCP): Reliably sending packets

## Slide 3: Review: IP Reliability
Reliability ensures that packets are received correctly
IP is unreliable and only provides a best effort delivery service, which means:
  Packets may be lost (“dropped”)
  Packets may be corrupted
  Packets may be delivered out of order
It is up to higher level protocols to ensure that the connection is reliable

## Slide 4: Scratchpad: Let’s Design It Together
Problem: IP packets have a limited size. To send longer messages, we have to manually break messages into packets
  When sending packets: TCP will automatically split up messages
  When receiving packets: TCP will automatically reassemble the packets
Problem: Packets can arrive out of order
  When sending packets: TCP labels each byte of the message with increasing numbers
  When receiving packets: TCP can use the numbers to rearrange bytes in the correct order
Problem: Packets can be dropped
  When receiving packets: TCP sends an extra message acknowledging that a packet has been received
  When sending packets: If the acknowledgement doesn’t arrive, re-send the packet

## Slide 5: Transmission Control Protocol (TCP)
Provides a byte stream abstraction
  Bytes go in one end of the stream at the source and come out at the other end at the destination
  TCP automatically breaks streams into segments, which are sent as layer 3 packets
Provides ordering
  Segments contain sequence numbers, so the destination can reassemble the stream in order
Provides reliability
  The destination sends acknowledgements (ACKs) for each sequence number received
  If the source doesn’t receive the ACK, the source sends the packet again
Provides ports
  Multiple services can share the same IP address by using different ports
Notes: In fact, the initial packets, ACK packets, and SYN-ACK packets, They are all TCP segments.

## Slide 6: Ports
Ports help us distinguish between different applications on the same computer or server
  On private computers, port numbers can be random
  On public servers, port numbers should be constant and well-known (so users can access the right port)
Remember: TCP is built on top of IP, so the IP header (and therefore the IP address) is still present
IP Header: send to: 1.2.3.4
TCP Header: send to: port 80
I am hungry.
Notes: Hammer in the concept that we build messages from high to low so headers of higher layers are put first into the message packets so therefore end up “below” the headers of the lower layers

## Slide 7: Establishing Sequence Numbers
Each TCP connection requires two sets of sequence numbers
  One sequence number for messages from the client to the server
  One sequence number for messages from the server to the client
Before starting a TCP connection, the client and server must agree on two initial sequence numbers (ISNs)
  The ISNs are different and random for every connection (for security reasons)
H | e | l | l | o |  | s | e | r | v | e | r
50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61
H | e | l | l | o |  | c | l | i | e | n | t
25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36
Messages from the client are numbered starting at 50.
Messages from the server are numbered starting at 25.

## Slide 8: TCP: 3-Way Handshake
Client chooses an initial sequence number x its bytes and sends a SYN (synchronize) packet to the server
Client
Server
SYN. Seq = x
SYN-ACK. Seq = y, Ack = x+1
ACK. Seq = x+1, Ack = y+1
Server chooses an initial sequence number y for its bytes and responds with a SYN-ACK packet
Client then returns with an ACK packet
Once both hosts have synchronized sequence numbers, the connection is “established”
Data

## Slide 9: TCP: Sending and Receiving Data
The TCP handlers on each side track which TCP segments have been received for each connection
  A connection is identified by these 5 values (sometimes called a 5-tuple)
    Source IP
    Destination IP
    Source Port
    Destination Port
    Protocol
Data from the bytestream can be presented to the application when all data before has been received and presented
  Recall: TCP presents data to the application as a bytestream, so the order must be preserved from one end to the other, even if packets are received out of order

## Slide 10: TCP: Sending and Receiving Data
Byte i of the bytestream is represented by sequence number x + i
  The first byte is byte i = 1, since sequence number x was used for the SYN packet and y for the SYN-ACK packet
A packet’s sequence number is the number of the first byte of its data
  This number is from the sender’s set of sequence numbers
A packet’s ACK number, if the ACK flag is set, is the number of the byte immediately after the last received byte
  This number is from the receiver’s set of sequence numbers
  This would be (sequence number) + (length of data) for the last received packet

## Slide 11: TCP: Sending and Receiving Data
Client
Server
ACK. Seq = x+1, Ack = y+1. Data, length A
ACK. Seq = y+1, Ack = x+1+A. Data, length B
ACK. Seq = x+1+A, Ack = y+1+B. Data, length C
ACK. Seq = y+1+B, Ack = x+1+A+C. Data, length D
Notes: TODO

## Slide 12: TCP: Retransmission
If a packet is dropped (lost in transit):
  The recipient will not send an ACK, so the sender will not receive the ACK
  The sender repeatedly tries to send the packet again until it receives the ACK
If a packet is received, but the ACK is dropped:
  The sender tries to send the packet again since it didn’t receive the ACK
  The recipient ignores the duplicate data and sends the ACK again
When packets are dropped in TCP, TCP assumes that there is congestion and sends the data at a slower rate

## Slide 13: TCP: Ending/Aborting a Connection
To end a connection, one side sends a packet with the FIN (finish) flag set, which should then be acknowledged
  This means “I will no longer be sending any more packets, but I will continue to receive packets”
  Once the other side is no longer sending packets, it sends a packet with the FIN flag set
To abort a connection, one side sends a packet with the RST (reset) flag set
  This means “I will no longer be sending nor receiving packets on this connection”
  RST packets are not acknowledged since they usually mean that something went wrong

## Slide 14: TCP Flags
ACK
  Indicator that the user is acknowledging the receipt of something (in the ack number)
  Pretty much always set except the very first packet
SYN
  Indicator of the beginning of the connection
FIN
  One way to end the connection
  Requires an acknowledgement
  No longer sending packets, but will continue to receive
RST
  One way to end a connection
  Does not require an acknowledgement
  No longer sending or receiving packets

## Slide 15: TCP Segment Structure
TCP segment header
Source Port (16 bits) |  |  |  | Destination Port (16 bits) |  |  | 
Sequence Number (32 bits) |  |  |  |  |  |  | 
Acknowledgement Number (32 bits) |  |  |  |  |  |  | 
Data Offset (4 bits) | Flags (12 bits) |  |  | Window Size (16 bits) |  |  | 
Checksum (16 bits) |  |  |  | Urgent Pointer (16 bits) |  |  | 
Options (variable length) |  |  |  |  |  |  | 
Data (variable length) |  |  |  |  |  |  | 
Notes: Notice: Ports, sequence number, ACK number, flags, checksum, and data

## Slide 16: TCP Attacks
TCP hijacking: Tampering with an existing session to modify or inject data into a connection
  Data injection: Spoofing packets to inject malicious data into a connection
    Need to know: The sender’s sequence number
    Easy for MITM and on-path attackers, but off-path attackers must guess 32-bit sequence number (called blind injection/hijacking, considered difficult)
    For on-path attackers, this becomes a race condition since they must beat the server’s legitimate response
  RST injection: Spoofing a RST packet to forcibly terminate a connection
    Same requirements as packet injection, so easy for on-path and MITM attackers, but hard for off-path attackers
    Often used in censorship scenarios to block access to sites

## Slide 17: TCP Data Injection
Client
Server
ACK. Seq = x+1, Ack = y+1. Data, length A
ACK. Seq = y+1, Ack = x+1+A. Real data, length B
This packet will be ignored by the client since the client already processed the malicious packet!
Seq = y+1. Evil data, length B
Notes: TODO

## Slide 18: TCP Spoofing
Client
Server
RST. Seq = x+1
SYN-ACK. Seq = y, Ack = x+1
SYN. Seq = x
ACK. Seq = x+1, Ack = y+1. Evil data
An on-path attacker must send the evil data before the server receives the real client’s RST!
A MITM attack could just drop the client’s packets, however
Notes: TODO

## Slide 19: TCP Attacks
TCP spoofing: Spoofing a TCP connection to appear to come from another source IP address
  Need to know: Sequence number in the server’s response SYN-ACK packet
  Easy for MITM and on-path attackers, but off-path attackers must guess 32-bit sequence number (called blind spoofing, also considered difficult)
  For on-path attackers, this is a race condition, since the real client will send a RST upon receiving the server’s SYN-ACK!

## Slide 20: TCP Attacks
TCP provides no confidentiality or integrity
  Instead, we rely on higher layers to prevent those kind of attacks
Defense against off-path attackers rely on choosing random sequence numbers
  Bad randomness can lead to trivial off-path attacks: TCP sequence numbers used to be based on the system clock!

## Slide 21: Summary
Transmission Control Protocol (TCP): Reliably sending packets
  3-way handshake: Client sends SYN, server sends SYN-ACK, client sends ACK
  Provides reliability, ordering, and ports
  Attack: TCP hijacking through data injection or RST injection
    Blind attacks must guess the client’s or server’s sequence numbers
  Attack: TCP spoofing by sending a spoofed SYN packet
    Blind attacks must guess the server’s sequence number