## Slide 1: Low Level Network Attacks

## Slide 2: Last Time: Intro to Networking
Internet: A global network of computers
  Protocols: Agreed-upon systems of communication
OSI model: A layered model of protocols
  Layer 1: Communication of bits
  Layer 2: Local frame delivery
    Ethernet: The most common Layer 2 protocol
    MAC addresses: 6-byte addressing system used by Ethernet
  Layer 3: Global packet delivery
    IP: The universal Layer 3 protocol
    IP addresses: 4-byte (or 16-byte) addressing system used by IP
  Layer 4: Transport of data (more on this next time)
  Layer 7: Applications and services (the web)
Application
Transport
(Inter) Network
Link
Physical
1
2
3
4
7

## Slide 3: Last Time: ARP
Classes of attackers:
  Off-path: Can’t see, modify, or drop packets
  On-path: Can see packets, but can’t modify or drop packets
  MITM: Can see, modify, and drop packets
ARP: A protocol to translate local IP addresses to MAC addresses
  Ask everyone on the network, “Who has the IP 1.2.3.4?”
  Attack: The attacker can respond instead of the true device with 1.2.3.4, and packets will get routed to the attacker!
  Defense: Switches
  Defense: Rely on higher layers

## Slide 4: Today: Low-Level Network Attacks
WPA: Communicate securely in a wireless local network
DHCP: Get configurations when first connecting to a network

## Slide 5: Dynamic Host Configuration Protocol (DHCP)

## Slide 6: DHCP: Initial Network Configuration
To connect to a network, a user needs:
  An IP address so that other people can contact the user
  The IP address of the DNS server (we’ll see this soon)
  The IP address of the router (gateway) so that the user can contact machines outside of the LAN
The first time a user connects, they don’t have this information yet
  The user also doesn’t know who to ask for this information
DHCP gives the user a configuration when they first join the network

## Slide 7: Steps of the DHCP Handshake
Client Discover: The client broadcasts a request for a configuration
DHCP Offer: Any DHCP server can respond with a configuration offer
  Usually only one DHCP server responds
  The offer includes an IP address for the client, the DNS server’s IP address, and the (gateway) router’s IP address
  The offer also has an expiration time (how long the user can use this configuration)
Client Request: The client broadcasts which configuration it has chosen
  If multiple DHCP servers made offers, the ones that were not chosen discard their offer
  The chosen DHCP server gives the offer to the client
DHCP Acknowledgement: The chosen server confirms that its configuration has been given to the client

## Slide 8: Dynamic Host Configuration Protocol (DHCP)
Alice
Bob
DHCP Server 1
DHCP Server 2
Router
Alice’s configuration | 
My IP | ???
DNS Server | ???
Gateway | ???
Alice wants to connect to the network, but she’s missing a configuration.

## Slide 9: Dynamic Host Configuration Protocol (DHCP)
Alice
Alice’s configuration | 
My IP | ???
DNS Server | ???
Gateway | ???
1. Client Discover: Alice broadcasts a request for a configuration.
Bob
DHCP Server 1
DHCP Server 2
Router
“Can anyone give me a configuration?”

## Slide 10: Dynamic Host Configuration Protocol (DHCP)
Alice
Bob
DHCP Server
DHCP Server
Router
Alice’s configuration | 
My IP | ???
DNS Server | ???
Gateway | ???
2. DHCP Offer: Any DHCP server can reply with an offer for Alice.
“You can use IP x, DNS server y, and gateway z”
“You can use IP a, DNS server b, and gateway c”

## Slide 11: Dynamic Host Configuration Protocol (DHCP)
Alice
Alice’s configuration | 
My IP | ???
DNS Server | ???
Gateway | ???
3. Client Request: Alice broadcasts which configuration she has chosen.
Bob
DHCP Server 1
DHCP Server 2
Router
“I’ll use DHCP Server 1”

## Slide 12: Dynamic Host Configuration Protocol (DHCP)
Alice
Alice’s configuration | 
My IP | x
DNS Server | y
Gateway | z
4. DHCP Acknowledgement: The chosen DHCP server confirms that the configuration has been set for Alice.
Bob
DHCP Server 1
DHCP Server 2
Router
Reserved for Alice: IP x, DNS y, gateway z

## Slide 13: DHCP Attacks
Alice has no way of verifying the DHCP response
  Spoofing: Any attacker on the network can claim to have a configuration
Alice usually expects only one DHCP server to respond, so she will accept the first response
  Race condition: As long as the attacker responds faster, Alice will accept the attacker’s response
DHCP attacks require Mallory to be in the same LAN as Alice
DHCP attacks let Mallory become a man-in-the-middle (MITM) attacker
  Mallory claims the gateway router’s address is Mallory’s address
    When Alice sends a message to the rest of the Internet, she actually sends it to Mallory
    Mallory can modify the message before sending it to its destination
  Mallory can also claim the DNS server’s address is Mallory’s address

## Slide 14: ARP and DHCP
The attacks on ARP and DHCP are very similar
  Spoofing: The attacker claims to have an answer
  Race condition: The requester accepts the first response. As long as the attacker’s response arrives first, it is accepted
Main vulnerabilities
  Broadcast protocols: Requests are sent to everyone on the LAN, so the attacker can see every request
  No trust anchor: There is no way to verify that responses are legitimate

## Slide 15: DHCP Defenses
DHCP is hard to defend against
  No root of trust: When we first connect, there’s nobody we can trust
Instead, we rely on defenses provided in higher layers

## Slide 16: Wireless Local Networks

## Slide 17: Wi-Fi
Wi-Fi: A layer 2 protocol that wirelessly connects machines in a LAN
  Alternative is Ethernet, which uses wires to connect machines in a LAN
Parts of a Wi-Fi network
  Access point: A machine that will help you connect to the network
  SSID (service set identifier): The name of the Wi-Fi network
  Password: Optionally, a password to secure Wi-Fi communications

## Slide 18: WPA2
Wi-Fi Protected Access 2 (WPA2): A protocol for securing Wi-Fi network communications with cryptography
Design goals
  Everyone with the Wi-Fi password can join the network
  Messages sent over the network are encrypted with keys
  An attacker who does not know the Wi-Fi network cannot learn the keys

## Slide 19: WPA Handshake
The client sends an authentication request to the access point
Client
Access Point
Derive PSK from wifi password
Derive PSK from wifi password
Authentication Request
ANonce
SNonce
Derive PTK from PSK, nonces, MAC addresses
Derive PTK from PSK, nonces, MAC addresses
MIC
MIC
GTK
ACK
Both use the password to derive the PSK (pre-shared key)
Both exchange random nonces
Both use the PSK, nonces, and MAC addresses to derive the PTK (pairwise transport keys)
Both exchange MICs (these are MACs from the crypto unit) to ensure no one has tampered with the nonces, and that the PTK was correctly derived
The access point encrypts and sends the GTK (group temporal key) to the client, used for broadcasts that anyone can decrypt
The client acknowledges receiving the GTK

## Slide 20: WPA Handshake
Both sides derive secret keys for communication
  Wi-Fi password → PSK
  PSK + nonces + MAC addresses → PTK
  The PTK is used to encrypt and authenticate all future communication
  Note: The PTK is different for every user, because of the nonces
The access point encrypts and sends the GTK to the client
  The GTK is used for messages broadcast to the entire network
  Everyone on the network uses the same GTK
The optimized version of the handshake decreases the number of messages sent back and forth

## Slide 21: Optimized WPA 4-Way Handshake
Client
Access Point
Derive PSK from wifi password
Derive PSK from wifi password
Authentication Request
ANonce
SNonce + MIC
Derive PTK from PSK, nonces, MAC addresses
Derive PTK from PSK, nonces, MAC addresses
MIC + GTK
ACK
The client sends an authentication request to the access point
Both use the password to derive the PSK (pre-shared key)
The AP sends ANonce to the client
The client generates SNonce, uses the PSK, nonces, and MAC addresses to derive the PTK (pairwise transport keys)
The client sends SNonce and its MIC to the AP
The AP uses the PSK, nonces, and MAC addresses to derive the PTK (pairwise transport keys)
The AP sends its MIC and GTK to the client
The client acknowledges receiving the GTK

## Slide 22: WPA-PSK Attacks
Rogue AP: Pretend to be an AP, and offer your own ANonce to the client
  If you know the password/PSK, you can complete the 4-way handshake with the client and become a MITM!
Client
Access Point
Derive PSK from wifi password
Derive PSK from wifi password
Authentication Request
ANonce
SNonce
Derive PTK from PSK, nonces, MAC addresses
Derive PTK from PSK, nonces, MAC addresses
MIC
MIC
GTK
ACK

## Slide 23: WPA-PSK Attacks
Offline brute-force attack: People tend to choose bad passwords, and you have enough information to know if you guessed the password correctly
  Nonces are sent unencrypted, and client and AP MAC addresses are public
  Eavesdropper guesses a password and derives:
    Wi-Fi password → PSK
    PSK + nonces + MAC addresses → PTK
    Eavesdropper checks that the MIC from the guess matches the MIC that was sent
Client
Access Point
Derive PSK from wifi password
Derive PSK from wifi password
Authentication Request
ANonce
SNonce
Derive PTK from PSK, nonces, MAC addresses
Derive PTK from PSK, nonces, MAC addresses
MIC
MIC
GTK
ACK

## Slide 24: WPA-PSK Attacks
No forward secrecy: An eavesdropper who records the values of ANonce and SNonce can derive the key if they later learn the password or PSK
  Compare to Diffie-Hellman: An eavesdropper can’t learn the key even if the record ga and gb and later compromise Alice’s computer
Client
Access Point
Derive PSK from wifi password
Derive PSK from wifi password
Authentication Request
ANonce
SNonce
Derive PTK from PSK, nonces, MAC addresses
Derive PTK from PSK, nonces, MAC addresses
MIC
MIC
GTK
ACK

## Slide 25: WPA-Enterprise
Core issue: Every client starts with the same PSK to derive the PTK
  Fix: Have each user use their own username and password, instead
    This is the model that AirBears2 and eduroam use!
Instead of using a PSK, use a randomly generated key by an authentication server
  For your client to trust the authentication server, you accept a digital certificate
  Form a secure channel to the authentication server, which lets you enter your username and password
  If the username and password are correct, the authentication server sends a one-time key to use instead of a PSK to both the client and the AP (also over a secure channel)
The rest of the handshake proceeds normally

## Slide 26: WPA-Enterprise Attacks
WPA Enterprise defends against the previous attacks
  Rogue AP attack: The APs must authenticate themselves to the server, which the attacker can’t do
  Brute-force attack: The generated PSK replacement is long and random, too long to brute-force
  No forward secrecy: The generated PSK replacement is used once and then discarded, so no information is retained that allows the PTK to be recovered later
However, it is still vulnerable to higher-layer attacks such as ARP or DHCP spoofing
  WPA is really a layer 1 protocol, so it can’t provide defenses for this!

## Slide 27: Border Gateway Protocol (BGP)
Textbook Chapter 29

## Slide 28: Review: Internet Protocol (IP)
Internet Protocol (IP): The universal layer-3 protocol that all devices use to transmit data over the Internet
IP address: An address that identifies a device on the Internet
  IPv4 is 32 bits (e.g. 35.163.72.93)
  IPv6 is 128 bits (e.g. 2607:f140:8801:0000:0000:0000:0001:0023)
    Shorthand: omit sets of zeros: 2607:f140:8801::1:23
  Globally unique from any single perspective
    For now, you can think of them as just being globally unique
  IP addresses help nodes make decisions on where to forward the packet

## Slide 29: Subnets
Recall: Layer 3 routes packets across multiple nodes on different LANs
  A packet might make many hops across different local networks before it can reach its destination
IP routes by subnets, which are groups of addresses with a common prefix
  A subnet is written as a prefix followed by the length of the prefix
    Example: 128.32.0.0/16 is an IPv4 subnet with all addresses that begin with the prefix of 128.32.*
    Since an IPv4 is a 32-bit address and there are 16 bits in the prefix, this subnet represents 232 - 16 = 216 addresses

## Slide 30: Routing Packets
To send a packet to a computer within the local network:
  Verify that the destination IP is in the same subnet
  Use ARP (or contact a switch) to get the destination MAC address
  Send the packet directly to the destination using the destination MAC address
To send a packet to a computer that is not within the local network:
  Send the packet to the gateway
  Past the gateway, the packet goes to the Internet
  It’s the gateway’s job to deliver the packet closer to the destination

## Slide 31: Autonomous Systems
Once your system sends the packet to the gateway, the packet has to be routed through the Internet
The Internet is a network of networks, comprised of many autonomous systems (AS)
  Each AS handles its own internal routing
  Each AS is uniquely identified by its autonomous system number (ASN)
  Each AS is comprised of one or more LANs
  The AS can forward packet to other connected ASes
The protocol for communicating between different Autonomous Systems is Border Gateway Protocol (BGP)
  Each router announces what networks it can provide and the path onward from the router
  The most precise route with the shortest path and no loops is the preferred route

## Slide 32: BGP
Sender
Recipient
AS 1
AS 3
AS 2
AS 5
AS 4
AS 6
I can reach {Recipient}
I can reach {AS6->Recipient}
I can reach {AS6->Recipient}
I can reach {AS4->AS6->Recipient}
I can reach {AS5->AS6->Recipient}
I can reach {AS4->AS6->Recipient}
Notes: Note that AS1 has a choice of whether to use AS2, AS3, or AS4. It chooses AS4 since AS4 provides the most direct path. If the AS1-AS4 link drops, AS1 will recalculate and choose either AS1->AS3->AS5->AS6 or AS1->AS2->AS4->AS6. So the decision of which path to choose is a dynamic problem that has to be continuously calculated. You cannot figure out the path before, thats the point of hop by hop.

## Slide 33: IP and BGP Attacks
Each AS implicitly trusts the surrounding ASes and accepts advertised routes
IP spoofing: Malicious clients can send IP packets with source IP values set to a spoofed value
  Edge ASes should block packets with source IPs set to the wrong value, but some don’t
  Enables packets that look like they’re coming from someone else!
  We rely on defenses provided by higher layers to further prevent this (“defense in depth”)
BGP hijacking: A malicious autonomous system can lie and claims itself to be responsible for a network which it isn’t
  Example: AS3 broadcasts that it is responsible for 128.32.0.0/16
    Now, the malicious AS can act as a MITM for traffic to 128.32.0.0!
  No real defenses on this level, so we rely on defenses from higher levels

## Slide 34: Summary
Classes of attackers:
  Off-path: Can’t see, modify, or drop packets
  On-path: Can see packets, but can’t modify or drop packets
  MITM: Can see, modify, and drop packets
ARP: A protocol to translate local IP addresses to MAC addresses
  Ask everyone on the network, “Who has the IP 1.2.3.4?”
  Attack: The attacker can respond instead of the true device with 1.2.3.4, and packets will get routed to the attacker!
  Defense: Switches
  Defense: Rely on higher layers
DHCP: A protocol for a new client to receive a network configuration
  Ask everyone on the network, “What is the network configuration to use?”
  Attack: The attacker can respond with a malicious configuration
  Defense: Rely on higher layers

## Slide 35: Summary
WPA: A protocol to encrypt Wi-Fi connections at layer 1
  Messages between the client and the AP are encrypted with keys
  Handshake uses MICs (cryptographic MACs) to verify that both parties have the same PSK and nonces
  WPA-PSK: Use a password to derive a PSK, which is used in a handshake to arrive at a key
    Attack: Attacker can pretend to be an AP
    Attack: Brute-force the password after recording a handshake
    Vulnerability: No forward secrecy
  WPA-Enterprise: Use a third party to provide a one-time “replacement PSK,” used in the same handshake
    Solves the attacks on WPA-PSK

## Slide 36: Summary
Border Gateway Protocol (BGP): Routing packets
  The Internet is made of smaller autonomous systems (AS)
  Each AS broadcasts the shortest routes it knows of (dependent on the shortest routes of its neighbors and distance to neighbors)